Displays

36 pin display requires excessive board space and is not viable.
Use two 12 pin devices, each with its own ATtiny861 drivers each containing 16 IO pins.
Slave device: 1 reset pin, 2 for the I2C and 1 spare: drives chars 7 to 4
Master device: 1 reset pin, 2 for the I2C and 1 for the brightness control: drives chars 3 to 0
Brightness control: Double click to increase it, single click to reduce it.
Control:
Master
Communicates with UNO to get number in long or double format.
Converts the number into characters
Illuminates char 7 and sends char 3 to slave
Moves on to chars 6 and 2 etc.
Slave:
Receives digit plus brightness
Illuminates digits starting with 3 then 2 etc.

Master I2C MSB DO: Brightness control			LSB I2C slave DO: unused
Dig 1 MSB	B0	1	Dig 1	B5	8
Dig 2	A5	13	Dig 2	B2	3
Dig 3	A6	12	Dig 3	B1	2
Dig 4	B6	9	Dig 4 LSB	B6	9
a	A3	17	a	B4	7
b	A7	11	b	B0	1
c	B4	7	c	A6	12
d	B2	3	d	A4	14
e	B1	2	e	A3	17
f	A4	14	f	B3	4
g	B5	8	g	A7	11
DP	B3	4	DP	A5	13

Reset	B7	10
DI (SDA)	A0	20
USCK (SCL)	A2	18
DO	A1	19

+5V	5,15
0V	6, 16

IC display interconnections: Selected to minimise board space.
MUX interrupt
timer_T0_sub_with_interrupt(T0_delay_4ms);}
8MHz Count from 0x7FFF to 0xFFFF (32768)
takes 4.096mS and gives flicker free operation for a four digit display.
Refresh rate 61 per second

The USI	This used timer 1 rather than timer 0.

Current per segment:

220R
Digit high level: 4.58V
Resistor drop 2.32V
Segment driver low level 0.24
Diode drop 2.02V
Calculate 10.5mA

110R
1.94V across resistor
Current is 17mA gives negligible extra light

Google search on “avr usi application notes”
and get AVR310: Using the USI module as a TWI master
AVR311 or AVR312: Using the USI Module as a I2C slave

Master implementation code
Go to	http://edge.rit.edu/content/P14254/public/Design/Electronics/Controller/Code/Atmel%20Application%20Notes
Click on	I2C	AVR310	GCC	AVR310 Using the USI module as a TWI master

Save the files	USI_TWI_Master.c	USI_TWI_Master.h	main.c
Slave SW
https://www.microchip.com/wwwAppNotes/AppNotes.aspx?appnote=en591197

ftoa() subroutines
See https://www.geeksforgeeks.org/convert-floating-point-number-string/
 for floating point number to askii subroutines

Splitting Arduino files into multiple ones:
I find this a bit fraught.
Propose to stick to my original solution using a resources folder even though Arduino may not be able to open its files.
Though the accepted answer works, I feel while the Arduino "IDE" is great for beginners but it doesn't quite scale well beyond a couple of files. I'd highly recommend checking out platformio as it provides much better project management via integration with atom and vscode, enables you to work with different frameworks including Arduino for AVR, STM32, ESP8266, ESP32 etc and supports debugging if you have the required hardware. – Shreyas Murali Jan 15 '19 at 19:39
10

TWI master operation

Clock sources:
T0 interrupt
USITC the software clock
USITC external clock

Writing to USITC toggles the level on the USCK/ SCL pin. This signal clocks the slave device.
It is also used to clock the master shift register containing the data byte

Assume that the open drain outputs invert the signal