Displays

36 pin display requires excessive board space and is not viable.
Use two 12 pin devices, each with its own ATtiny861 drivers each containing 16 IO pins.
Slave device: 1 reset pin, 2 for the I2C and 1 spare: drives chars 7 to 4
Master device: 1 reset pin, 2 for the I2C and 1 for the brightness control: drives chars 3 to 0
Brightness control: Double click to increase it, single click to reduce it.
Control:
Master
Communicates with UNO to get number in long or double format.
Converts the number into characters
Illuminates char 7 and sends char 3 to slave
Moves on to chars 6 and 2 etc.
Slave:
Receives digit plus brightness
Illuminates digits starting with 3 then 2 etc.

Master I2C MSB DO: Brightness control			LSB I2C slave DO: unused
Dig 1 MSB	B0	1	Dig 1	B5	8
Dig 2	A5	13	Dig 2	B2	3
Dig 3	A6	12	Dig 3	B1	2
Dig 4	B6	9	Dig 4 LSB	B6	9
a	A3	17	a	B4	7
b	A7	11	b	B0	1
c	B4	7	c	A6	12
d	B2	3	d	A4	14
e	B1	2	e	A3	17
f	A4	14	f	B3	4
g	B5	8	g	A7	11
DP	B3	4	DP	A5	13

Reset	B7	10
DI (SDA)	A0	20
USCK (SCL)	A2	18
DO	A1	19

+5V	5,15
0V	6, 16

IC display interconnections: Selected to minimise board space.